## Slide 1: MINIMISATION OF TUNNEL OVERBREAK IN DRILL AND ROCK BLAST TUNNELLING
Guided by Presented by
Dr R. Senthil Kumar, P. Vishnu Vardhan
Assistant professor M Tech, Construction Technology & Management
Dept of Civil Engineering 203519019
Sanjay Pajni,
Chief Engineering Manager , EDRC Faridabad, Larsen & Toubro

## Slide 2: INTRODUCTION
In the last part of the project, blasting practises at RVNL site were studied and certain relations of blasting parameters with overbreak were formulated. Those are:
Overbreak= 3.8507+0.1187(OI)
OB=0.54(Cf/Q)+5.80;
OB=5.22ln(qp/Af)+ 7.57;
The above developed equations involve blasting parameters, tunnel characteristic features and geological parameter in the form of Q.
Overbreak volume can be divided into geological overbreak ( excess rock break due to release of in situ stress or due to orientation of discontinuities), blast induced overbreak ( excess rock break due to inaccuracy in drilling and charging of contour blast holes, which control the damage induced in the surrounding rock mass due to blasting.
Apart from Q (which is a function of 6 geological parameters) there are other important geological parameters which were not included in the model.
This part of the project proceeds forward with an intention to define overbreak in terms of other geological properties.
The properties in interest are PPV (peak particle velocity), HCF (half cast factor) and ONORM rock classes.

## Slide 3: OBJECTIVE AND SCOPE
OVERBREAK CAUSING FACTORS
BLASTING
GEOLOGICAL
TUNNEL CHARACTERISTICS
AREA OF STUDY
This part of project circles around defining overbreak in terms of geological parameters and finding out the relation between them.
The main objectives are :
Defining threshold PPV levels for different explosives and rock conditions, thereby defining extent of rock damage
Classifying overbreak with usage of half cast factor into blast induced overbreak and geological overbreak for risk sharing purpose

## Slide 4: LITERATURE REVIEW
AUTHOR’S NAME | WORK DONE
Murthy & Dey (2003) | Reported a ground vibration predictor equation including the effect of free face in tunnel blasting in terms of distance from blast hole, maximum charge density.
Holmberg & perrson (1979) | For an extended charge of charge length ‘H’ of linear charge concentration of l (kg/m), an approximation of the resulting velocity has been obtained by integrating the generalized equation for the total charge length after dividing it into small parts.
Forsyth and Moss (1990) | They devised a method of quantifying blast induced damage. Their proposed Drift Condition Rating (DCR) comprised two components: firstly, the drift back condition (related to the rock mass integrity and the percentage of half cast visible); and secondly, the amount of overbreak.
Yu and Vongpaisal (1996) | They proposed a new blast damage criteria based on dynamic tensile strength, compressional wave velocity (P-wave), density of rock mass and peak particle velocity of the blast
Silva et al (2019) | using the Holmberg and Personn (HP model formula) PPV and Fleetwood and Forsyth considerations for rock strength developed a practical mode of assessing rock damage. This method includes measuring the PPV using geophones from a distance. Then using the Fleetwood and Forsyth formula maximum tolerable PPV is defined.

## Slide 5: LITERATURE REVIEW (CONTINUED)
AUTHOR’S NAME | WORK DONE
Singh et al(1992) | They used half cast factor as a measure of blast-induced overbreak. Half cast factor is the ratio of total visible drill mark length in the wall and roof after blast to the total drilling length. This was used as indicator of blasting performance.
Voza et al (2019) | Used the half cast factor as a tool to differentiate between the geological overbreak and blast induced overbreak. This classification was then used to define the limits for geological overbreak which enabled proper risk sharing between client and company.

## Slide 6: METHODOLOGY
COLLECTING DATA REQUIRED (MEASURED PPV VALUES, UCS (Unconfined compressive strength), young's modulus etc) FROM SITES
PREPARING USABLE CHARTS WHICH CAN BE USED TO PREDICT OVERBREAK DEPTH FROM THE BORE HOLE USING PPV ANALYSIS BY HP MODEL
HALF CAST FACTOR ANALYSIS TO DISTINGUISH TWO KINDS OF OVERBREAK.
PEAK PARTICLE VELOCITY ANALYSIS
PREPARING AN OVERBREAK PREDICTING MODEL BASED ON HALF CAST FACTOR ANAYSIS
PERFORMING CYCLE TIME ANALYSIS FOR LIVE CASES WHERE SMOOTH BLAST RECOMMENDATIONS MADE IN LAST PHASE WHERE APPLIED

## Slide 7
WORK DONE

## Slide 8: Cycle Time Analysis
Overbreak control measures using controlled blast techniques developed in the last semester (which included change in spacing and burden of perimeter holes, explosive charge density) is applied to site.
The reduced overbreak on an average is around 13% for rock class B2, 17 % for rock class B3, 9% for rock class C2, 8.5% for rock class C3 as seen in the previous semester.
The proposed measures led to decrease in overbreak, but the additional time taken in applying the control blast techniques should be considered as tunnelling engineers would not be willing to adopt the guideline if operation time may increases although overbreak decreases.
So it is absolutely necessary to perform time analysis and find out the new time taken for progression of tunnel.
In this study, the cycle time for each cycle has been collected from daily progress reports, based on which the average cycle time for each task has been calculated. Tunnels which are being studied belong to poor rock classification varies from B1, B2, B3, &C2, with B1 comparatively good rock than B2 and so on.
The majority of tunnels come under B2 and B3 types of rock. The other types of rocks are neglected in this study. Further analysis will be carried based on B2 and B3 types of rocks.

## Slide 9: Cycle Time Analysis
Analysis is carried in 4 parts namely, cycle time analysis for B2 class rock in main tunnels, B3 class rock in escape tunnels, B2 class rock in main tunnels and B3 class rock in escape tunnels.
B2 rock class | MT2 | MT2 (after application) | MT3 | MT3 (after application)
Activities | Average time (min) | Average time (min) | Average time (min) | Average time (min)
Preparation & Profile Marking | 17.01 | 25.5 | 94.10 | 26.3
Drilling | 81.04 | 100.35 | 65.57 | 90.60
Explosive Charging and Blasting | 61.84 | 62.5 | 56.01 | 75.62
De-fuming | 14.28 | 15.12 | 21.37 | 22.05
Mucking | 120.55 | 86.7 | 132.39 | 103.65
Scaling/Chipping/Breaking | 56.53 | 42.3 | 84.03 | 69.24
Face logging /Geological Mapping | 19.79 | 19.5 | 26.11 | 24.5
Rock support | 759.75 | 690 | 568.96 | 495
Total cycle time for a metre progress | 1130.79 | 1041.97 | 1048.54 | 906.96

## Slide 10: Cycle Time Analysis
The next analysed tunnels are same main tunnels 2 and 3 of class B3
B3 rock class | MT2 | MT2 (after application) | MT3 | MT3 (after application)
Activities | Average time (min) | Average time (min) | Average time (min) | Average time (min)
Preparation & Profile Marking | 75.27 | 90.5 | 18.97 | 26.3
Drilling | 85.71 | 110.35 | 86.18 | 105.45
Explosive Charging and Blasting | 56.57 | 69.49 | 64.2 | 65.7
De-fuming | 21 | 22 | 13.87 | 13.98
Mucking | 122.53 | 90.5 | 152.62 | 113.65
Scaling/Chipping/Breaking | 129.71 | 106.3 | 75.24 | 60.24
Face logging /Geological Mapping | 30 | 29 | 17.73 | 17.6
Rock support | 706.79 | 634.5 | 831 | 795
Total cycle time for a metre progress | 1227.59 | 1152.64 | 1259.8 | 1197.92

## Slide 11: Cycle Time Analysis
The next analysed tunnels are exit tunnels 2 and 3 but of superior rock class B2
B2 rock class | ET2 | ET2 (after application) | ET3 | ET3 (after application)
Activities | Average time (min) | Average time (min) | Average time (min) | Average time (min)
Preparation & Profile Marking | 21.80 | 26.5 | 73.99 | 88.34
Drilling | 58.75 | 80.35 | 62.26 | 85.67
Explosive Charging and Blasting | 45.29 | 48.65 | 43.27 | 44.14
De-fuming | 15.89 | 15.12 | 20.55 | 21.05
Mucking | 102.21 | 68.74 | 140.55 | 114.28
Scaling/Chipping/Breaking | 52.01 | 39.54 | 42.20 | 27.61
Face logging /Geological Mapping | 18.02 | 18.15 | 27.40 | 27.04
Rock support | 617.33 | 548.4 | 475.49 | 401.25
Total cycle time for a metre progress | 931.28 | 845.45 | 885.70 | 809.38

## Slide 12: Cycle Time Analysis
The next analysed tunnels are same exit tunnels 2 and 3 but of rock class B3
B3 rock class | ET2 | ET2 (after application) | ET3 | ET3 (after application)
Activities | Average time (min) | Average time (min) | Average time (min) | Average time (min)
Preparation & Profile Marking | 62.82 | 76.65 | 24.62 | 28.3
Drilling | 65.55 | 78.35 | 58.70 | 75.45
Explosive Charging and Blasting | 52.57 | 51.74 | 55.08 | 58.7
De-fuming | 16.99 | 16.56 | 17.24 | 16.56
Mucking | 100.57 | 70.15 | 114.33 | 76.25
Scaling/Chipping/Breaking | 80.30 | 59.14 | 56.9 | 42.85
Face logging /Geological Mapping | 25.96 | 24.69 | 19.70 | 19.6
Rock support | 506.27 | 419.65 | 751.58 | 670.65
Total cycle time for a metre progress | 911.04 | 796.93 | 1098.16 | 988.36

## Slide 13: Cycle Time Analysis
Due to application of these techniques drilling and profile marking took more time than the usual but because of less rock blasted mucking time and scaling, chipping time reduced.
Another major time reduction was seen in rock support installation courtesy of limited damage to surrounding rock.
The result is summarised as follows for main tunnels and exit tunnels.
Rock Class | MT2 cycle time (mins) |  | Reduced time (hr) | MT3 cycle time (mins) |  | Reduced time(hr)
 | Before | After |  | Before | After | 
B2 | 1130.79 | 1041.97 | 1.48 | 1048.54 | 906.96 | 2.35
B3 | 1227.59 | 1152.64 | 1.24 | 1259.8 | 1197.92 | 1.03

## Slide 14: Cycle Time Analysis
As seen from the above conclusions there is reduction in cycle times pre and post application of control blast techniques.
One striking point in the analysis apart from cycle time reduction is influence of rock class. As seen in both main tunnels and exit tunnels there is reduction of cycle time but the magnitude of reduction is greater for good rock class B2 as compared to B3.
This proves the fact that in a same tunnel when a superior rock is encountered optimised use of blasting techniques will often lead to less damage.

## Slide 15: PPV RELATION WITH OVERBREAK
Peak particle velocity is the velocity in the surrounding rock mass produced by the exploding charge in the borehole.
The selection of particle velocity as a parameter is because of the simplicity in measuring it using conventional geophones. When PPV is used as a parameter, the damage zone is calculated as the distance between the borehole and the location in the rock mass where the PPV value doesn’t cause any fracturing or damage in the intact rock/rock mass.
PPV value obtained from site is compared against a PPV value that is known or adopted (most of the time based on site specific field tests) that will produce some damage in the rock or rock mass.
The model going to be used is the Holmberg & perrson model. It is a function of distance from borehole centre and maximum charge per delay blast.
It is given by
PPV = peak particle velocity
Q= maximum charge per delay blast
R = distance from bore hole centre.
K, α, ß are site constants.

## Slide 16: DETERMINING SITE CONSTANTS
First step in the analysis is to determine site constants K, α, ß . They are found out from PPV measured at site using geophones from centre of a blast hole.
Chart: distance from centre
| -0.39031250000000206 | -0.77546874999999815 | 1.0732812500000009 | 3.0760937500000018 | -0.23625000000000007 | 0.22593749999999968 | -0.69843749999999982 | 0.68812499999999943 | 0.76515625000000043 | 2.1517187499999997 | 1.5354687499999979 | 0.6110937500000011 | 2.0746874999999987 | 1.5354687499999979 | -0.23625000000000007 | -2.3160937500000003 | 0.76515625000000043 | 0.53406249999999744 | -1.3917187500000008 | -0.4673437499999995 | -1.1606249999999996 | 0.45703125 | 0.99624999999999986 | 0.45703125 | 7.1874999999997691E-2 | -1.2376562500000006 | 0.30296874999999801 | 0.14890624999999869 | -0.77546874999999815 | -0.69843749999999982 | 0.76515625000000043 | -0.77546874999999815 | 1.7665625000000009 | 0.53406249999999744
 | 854 | 780 | 920 | 1082 | 863 | 843 | 863 | 850 | 886 | 982 | 921 | 878 | 974 | 922 | 845 | 732 | 934 | 913 | 803 | 771 | 832 | 863 | 891 | 843 | 820 | 780 | 855 | 863 | 780 | 854 | 903 | 828 | 926 | 822
This is the relation for PPV produced due to the blast on either side of blast hole.
PPV variation with distance is fitted using a straight line. As per HP model the intercept of the line is the Value of k and the slope value divided by 100 is the value of α. The other constant ß is taken as twice of α.
From the graph intercept is 852 which is the constant k. slope of the line is 54.192. α becomes 0.54. ß is twice the α which is 1.08
K=852, α=0.54, ß=1.08.

## Slide 17: DEFINING TRESHOLDS
The overbreak analysis was therefore carried in 4 tunnels.
Final area of tunnel to be formed:
main tunnel 2 & 3 = 60m2
escape tunnel 2 & 3 = 30m2
The major rock classes found in these 4 tunnels are B1,B2,C1,C2 ONORM class
The rock properties for each class are provided below
PARAMETER | VALUE
SPECIFIC GRAVITY | 2.68
LONGITUDINAL PROPOGATION VELOCITY (m/sec) | 5550
UCS(Pa) | 224
Youngs modulus(Gpa) | 21.4
PARAMETER | VALUE
SPECIFIC GRAVITY | 2.64
LONGITUDINAL PROPOGATION VELOCITY (m/sec) | 5120
UCS(Pa) | 210
Youngs modulus(Gpa) | 20.6
B2 CLASS
B3 CLASS

## Slide 18: DEFINING TRESHOLDS
PARAMETER | VALUE
SPECIFIC GRAVITY | 2.61
LONGITUDINAL PROPOGATION VELOCITY (m/sec) | 5020
UCS(MPa) | 202
Youngs modulus(Gpa) | 20.1
PARAMETER | VALUE
SPECIFIC GRAVITY | 2.59
LONGITUDINAL PROPOGATION VELOCITY (m/sec) | 4910
UCS(MPa) | 197
Youngs modulus(Gpa) | 19.6
C1 CLASS
C2 CLASS
As per Forsyth, PPV threshold = 0.1*UCSdynamic * longitudinal velocity / Youngs modulus.
UCSdynamic = strength factor * UCS static
strength increase factor for the different types of rock class (B1,B2,C1,C2) is 2.8 for B1, 2.9 for B2, 3.2 for C1, 3.4 for C2. (from GBR Of RVNL).
ROCK CLASS | PPV threshold (m/sec)
B2 | 16.65
B3 | 15.65
C1 | 15.13
C2 | 14.80

## Slide 19
PPV vs Distance around bore hole
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4
PPV vs R | 28.8399 | 13.6421 | 8.8045 | 6.4531 | 5.0712 | 4.1648 | 3.5261 | 3.0525
Rock class B2, whose Q=170 kg
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4
PPV vs R | 25.4643 | 12.0454 | 7.7739 | 5.6978 | 4.4776 | 3.6773 | 3.1133 | 2.6952
Rock class B3, whose Q=135 kg
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4
PPV vs R | 23.8952 | 11.3031 | 7.2949 | 5.3467 | 4.2017 | 3.4507 | 2.9215 | 2.5291
Rock class C1, whose Q=120 kg
Rock class C2, whose Q=110 kg
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4
PPV vs R | 22.7984 | 10.7843 | 6.9601 | 5.1013 | 4.0088 | 3.2923 | 2.7874 | 2.4131

## Slide 20: PPV (vs) Distance around bore hole
Once we have the PPV vs the distance around drilled hole for a rock type, we can read the damage limit corresponding to a particular PPV threshold value.
For example threshold PPV corresponding to rock class B2 is 16.65m/sec. when read against its PPV vs distance graph the extent of rock damage is 0.83m.
Similarly the rock damage depth on sides of borehole can be calculated for the threshold PPV fixed for any rock class from the graphs.
For minimisation we can work it the opposite way and find the corresponding PPV and from it the subsequent explosive to control the overbreak to a given extent can be determined.

## Slide 21: Half cast factor( HCF)
Half Cast Factor (HCF) is a popular parameter for the assessment of induced damage.
Controlled-blasting techniques leave intact almost half the blast hole surface, referred to as “half-casts” or “half barrels”. Half casts are the traces of blast holes on the excavated surfaces, and they are associated with radial fractures, provoking a blast-induced damage thickness.
It is computed as the total length of visible half-casts divided by the total length of drilled contour blast holes, and is typically expressed as a percentage.
HCF = * 100
Li = visible half cast
Lr = drilled hole length
Post blast profile showing half casts ; saiang (2008)

## Slide 22: Distinction of overbreak using HCF
Overbreak as mentioned earlier is classified into two types; blast induced and geological.
The application of half cast factor to differentiate is feasible only due to the implementation of the smooth blasting which is the case here. (which uses less energy which shows the half casts)
The Half cast developed by the Swedish Rock Engineering Research , was applied to differentiate between blast-induced overbreak and that associated with other sources , either natural or stress-induced.
When the overbreak occurred in a zone of visible half casts (HCF > 5%), then technical overbreak was indicated as the main component; (indicating the inefficient use of explosive energy).
On the contrary, when the overbreak was observed in the absence of visible half-casts (HCF = 0 to 5 %), it was assumed to be influenced by geological aspects. The application of this procedure was practically feasible due to the implementation of the smooth blasting.
The first step of the work consisted in investigating the possible correlations among technical overbreak and geological overbreak values and the main factors influencing the technical and geological overbreak.

## Slide 23: Factors studied
Out of the various geological factors discussed earlier, the factors which has variations in the given project site were studied. They are:
Length of blast hole
Discontinuity per round length
Spacing between discontinuities
Rock quality designation (RQD)
Rock mass rating
All the parameters studied were taken from main tunnel 2 &3 and escape tunnel 3.
The profiles of the tunnel cross section post blast are monitored using the Amberg software which delimits the areas with little to minimum half casts on the contour.
The allowable half casts in this project is taken around 5%.
Overbreak with HCF value above 5% were taken as technical overbreak and less than that is taken as geological overbreak.

## Slide 24: Relation between parameters and overbreak
First parameter studied is blast hole length. As defined earlier it is the length of horizontal the hole drilled into the available free face.
Chart: Overbreak vs Blast hole length
| 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 4
Overbreak vs Blast hole length | 0.03 | 0.032 | 0.036 | 0.032 | 0.033 | 0.035 | 0.036 | 0.034 | 0.034 | 0.033 | 0.04 | 0.033 | 0.038 | 0.038 | 0.044 | 0.042 | 0.039 | 0.04 | 0.042 | 0.042 | 0.044 | 0.043 | 0.045 | 0.042 | 0.044 | 0.048 | 0.05 | 0.047 | 0.048
Chart: Geo overbreak vs blast hole length
| 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 4 | 4
 | 0.0015 | 0.001 | 0.0012 | 0.0014 | 0.016 | 0.001 | 0.0012 | 0.0018 | 0.002 | 0.003 | 0.004 | 0.0015 | 0.0018 | 0.002 | 0.0022 | 0.0024 | 0.003 | 0.0035 | 0.0044 | 0.0062 | 0.001 | 0.015 | 0.022 | 0.024 | 0.034 | 0.038 | 0.039
The graphs explores the relationship between technical and geological overbreak .
Blast hole lengths drilled for B1 and B2 range 1.5 to 2m, while for C2 class the value is around 3m and 4m for class C3
Greater the blast hole length, greater the amount of explosive used. It by default indicates a good co-relation between technical overbreak and blast hole length

## Slide 25: Relation between parameters and overbreak
Second parameter studied is the discontinuity per round length. Number of discontinuities indicated the structural integrity of a rock (how intact the rock is in between the successive tunnel faces)
Chart: technical overbreak vs discontinuties per round length
| 1.5 | 1.5 | 1.5 | 1.5 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 5 | 5 | 5 | 5 | 5 | 6 | 7 | 8
Ob tech | 0.02 | 0.038 | 0.042 | 0.051 | 0.032 | 0.038 | 0.042 | 0.046 | 0.05 | 0.025 | 0.028 | 0.032 | 0.038 | 0.042 | 0.046 | 0.05 | 0.07 | 0.03 | 0.04 | 0.048 | 0.052 | 0.064 | 0.045 | 0.05 | 0.038
Chart: Geo overbreak vs discontinuties for Round length
| 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 6 | 7 | 8
discon | 0.01 | 0.015 | 0.03 | 0.034 | 0.006 | 0.009 | 0.011 | 0.018 | 0.023 | 0.027 | 0.004 | 0.012 | 0.015 | 0.018 | 0.02 | 0.03 | 0.038 | 0.007 | 0.01 | 0.015 | 0.021 | 0.022 | 0.038 | 0.058 | 0.04 | 0.03 | 0.05
As seen in both the cases higher is the number of discontinuities, greater is the overbreak.
Most of the higher number of discontinuities are of rock class C3 and C2.
Most of the tunnel length consists of rock class B2, B3 where the number of discontinuities are 3 to 5.

## Slide 26: Relation between parameters and overbreak
The third parameter studied is spacing between the discontinuities density in a round length. This is defined as number of discontinuities per round length. It indicates the denseness of a rock.
Chart: OB tech vs discontinuities density
| 0.6 | 0.6 | 0.8 | 0.7 | 2 | 2 | 2 | 2 | 2 | 2.1 | 2.1 | 2.1 | 2.2000000000000002 | 2.2000000000000002 | 2.2000000000000002 | 3
OB tech | 0.025 | 0.035 | 0.04 | 0.08 | 0.02 | 0.03 | 0.04 | 0.045 | 0.05 | 0.06 | 0.065 | 0.07 | 0.075 | 0.08 | 0.08 | 0.05
Chart: Ob geo vs discontinuities density
| 0.2 | 0.6 | 0.6 | 0.6 | 0.6 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2.1 | 2.2000000000000002 | 2.2000000000000002 | 2.2000000000000002 | 2.2000000000000002 | 2.2000000000000002 | 3
Ob geo | 0.02 | 0.005 | 0.01 | 0.015 | 0.02 | 0.005 | 0.005 | 0.01 | 0.015 | 0.02 | 0.025 | 0.03 | 0.035 | 0.04 | 0.045 | 0.045 | 0.06 | 0.07 | 0.02
Higher Discontinuity density is associated with rock class C2, C3 . It means higher number of discontinuities per unit length.
Higher the number, weaker the rock which indicates easy rock breakage causing higher overbreak
Blast design is usually made in accordance to geology, so the contribution to the total overbreak will come from geological part of it.

## Slide 27: Relation between parameters and overbreak
Next parameter studied is the rock quality designation . It indicates the soundness of the rock. It is one of prominent characteristic of Q- value. In this analysis it is used as Q- value representative.
Chart: OB tech vs RQD %
| 25 | 25 | 25 | 52 | 75 | 73 | 70 | 69 | 75 | 76 | 74 | 73 | 72 | 70 | 69 | 67 | 66 | 65 | 64 | 90 | 89 | 92 | 95 | 94 | 93
OB tech | 0.023 | 0.061 | 0.08 | 0.06 | 0.02 | 0.024 | 0.029 | 0.031 | 0.0345 | 0.038 | 0.042 | 0.048 | 0.051 | 0.054 | 0.059 | 0.062 | 0.065 | 0.068 | 0.072 | 0.03 | 0.045 | 0.05 | 0.06 | 0.08 | 0.075
Chart: Ob geo vs RQD %
| 25 | 25 | 25 | 45 | 45 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 90 | 89 | 84 | 89 | 87 | 85 | 90
Ob geo | 0.005 | 0.02 | 0.03 | 0.008 | 0.026 | 0.001 | 0.005 | 0.01 | 0.015 | 0.018 | 0.02 | 0.03 | 0.035 | 0.038 | 0.04 | 0.048 | 0.05 | 0.06 | 0.01 | 0.015 | 0.018 | 0.02 | 0.025 | 0.028 | 0.03
RQD indicates the rock resistance to drilling.
Higher the RQD value, lower is the number of discontinuities.
Higher RQD is often associated with rock class B2, B3
Rock with higher RQD when subjected to a properly designed blast design will not leave behind any half cast.
When a half cast is left behind for a high RQD rock , it indicates the defective blast design.

## Slide 28: Relation between parameters and overbreak
Last parameter studied is the rock mass rating. It is one of the three rock mass classification used in the project. It consists of 7 separate characteristics, so its effect on overbreak is explored
Chart: Ob geo vs RMR
| 52 | 62 | 65 | 66 | 68 | 69 | 70 | 71 | 73 | 72 | 72 | 73 | 76 | 74 | 75 | 75 | 74 | 74 | 76 | 76 | 78 | 79 | 79 | 80 | 81 | 82 | 85
Ob geo | 0.06 | 0.05 | 0.032 | 0.034 | 0.06 | 0.01 | 0.008 | 0.002 | 0.004 | 0.02 | 0.026 | 0.028 | 0.004 | 0.015 | 0.014 | 0.016 | 0.025 | 0.05 | 0.018 | 0.022 | 0.03 | 0.01 | 0.015 | 0.02 | 0.025 | 0.023 | 0.01
Chart: Overbreak technical vs RMR
| 52 | 60 | 66 | 65 | 64 | 69 | 70 | 71 | 74 | 72 | 74 | 75 | 75 | 76 | 79 | 79 | 80 | 72 | 73 | 74 | 77 | 77 | 78 | 78 | 81 | 82 | 84 | 67 | 73
Overbreak vs RMR | 0.058 | 0.04 | 0.03 | 0.038 | 0.04 | 0.03 | 0.028 | 0.031 | 0.027 | 0.024 | 0.026 | 0.022 | 0.021 | 0.025 | 0.015 | 0.016 | 0.018 | 0.028 | 0.03 | 0.027 | 0.024 | 0.028 | 0.022 | 0.021 | 0.018 | 0.02 | 0.018 | 0.035 | 0.029
Similar to RQD, RMR also rates the rock quality (more comprehensively) which considers the stress reduction factor due to opening.
High RMR indicates sound rock which requires higher blast energy to break rock.
High RMR demands more explosive energy prompting engineer to drill large hole lengths.
When overdone this results in misuse of explosive energy, leaving behind half casts

## Slide 29: Correlation between parameters and overbreak
For all the parameters observed, corelation was found out using excel stat (an add in to excel for statistics)
Corelation co-efficient for all the parameters are presented below.
Parameter | Technical Overbreak | Geological overbreak
Blast hole length | 0.89 | 0.22
Discontinuity number | -0.24 | 0.42
Discontinuity density | 0.14 | 0.31
RQD | -0.17 | 0.18
RMR | 0.35 | -0.87
The table above shows that technical overbreak is highly co-related with blast hole length while the geological overbreak is co-related with RMR.
Negative corelation of RMR with geological overbreak indicates the influence of geology on overbreak (less RMR corresponds to poor rock).

## Slide 30: Correlation between parameters and overbreak
Blast hole length and RMR index were therefore identified as those parameters most affecting the overbreak phenomenon and as such selected for further analyses.
Several regression models were attempted to find the best fit, quantified by the determination coefficient R2, between the specific technical overbreak and blast hole length, on one side, and the specific geological overbreak and the RMR index, on the other side.
Chart: 
| 52 | 60 | 66 | 65 | 64 | 69 | 70 | 71 | 74 | 72 | 74 | 75 | 75 | 76 | 79 | 79 | 80 | 72 | 73 | 74 | 77 | 77 | 78 | 78 | 81 | 82 | 84 | 67 | 73
Overbreak vs RMR | 0.058 | 0.04 | 0.03 | 0.038 | 0.04 | 0.03 | 0.028 | 0.031 | 0.027 | 0.024 | 0.026 | 0.022 | 0.021 | 0.025 | 0.015 | 0.016 | 0.018 | 0.028 | 0.03 | 0.027 | 0.024 | 0.028 | 0.022 | 0.021 | 0.018 | 0.02 | 0.018 | 0.035 | 0.029
Chart: Overbreak vs Blast hole length
| 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 4
Overbreak vs Blast hole length | 0.03 | 0.032 | 0.036 | 0.032 | 0.033 | 0.035 | 0.036 | 0.034 | 0.034 | 0.033 | 0.04 | 0.033 | 0.038 | 0.038 | 0.044 | 0.042 | 0.039 | 0.04 | 0.042 | 0.042 | 0.044 | 0.043 | 0.045 | 0.042 | 0.044 | 0.048 | 0.05 | 0.047 | 0.048

## Slide 31: Overbreak Model
The relationship between overbreak(technical) and geological overbreak with blast hole length and RMR respectively is established in above 2 graphs.
Different fits of curve for both the graphs are observed to determine the best fit
Model | Regression of OB tech on blast hole length | Regression of OB geo on RMR
Linear | 0.78 | 0.88
Logarithmic | 0.74 | 0.9
Power | 0.83 | 0.83
exponential | 0.80 | 0.84
Results of various regressions models are summarized in the above table
It shows that in the technical overbreak case the best fit is given by a power law while in the case of geological overbreak by a logarithmic law
an integrated model, given by the linear combination of the two models, was set up for the calculation of the specific total overbreak: OB = A* (L blast)B + C*ln(RMR) + D

## Slide 32: Constants Calculation
OB = A* (L blast)B + C*ln(RMR) + D.
This above equation is the summation of both geological and technical overbreak.
Since equation contains non linear terms, non – linear multiple regression is to be performed.
A, B, C, D are the constants which are to be determined.
The four parameters were calculated taking into account only the data collected in the Main tunnel 2 and escape tunnel 2,3 thus disregarding the data available for main tunnel 3.
Tunnel 3 data is used further for validation of models.
a nonlinear multiple regression analysis was performed. Initial values of the four regression parameters were set equal to the corresponding ones of the single power and logarithmic regressions of above graphs.
From the relations established, A= 0.0277, B = 0.3762, C = -0.083, D=0.3843. These are used as initial guess in the analysis.
An algorithm called Levenberg–Marquardt algorithm (one of the algorithms for non – linear multiple regression) in excel stat is used for constants determination.
This algorithm is based on differential equations, requiring the calculation of the partial derivatives of main equation with respect to the unknown parameters A,B,C,D

## Slide 33: Constants Calculation
Partial derivatives of equation with respect to constants are
The threshold limit of 0.02 for allowed standard deviation for each parameter is set.
The analysis is carried out until the standard deviation of all the parameters is less than 0.02.
The result of 1st iteration is as shown below
Parameter | Estimation | Standard deviation
A | 0.034 | 0.004
B | 0.216 | 0.108
C | -0.017 | 0.016
D | 0.125 | 0.056
After the first iteration, the standard deviations of the parameters A and C were found to be below the threshold while those of parameters B and D were well above. A second step was therefore necessary: the A and C parameters were fixed, while the calculation was repeated over the B and D parameters.

## Slide 34: Constants Calculation
Parameter | Estimation | Standard deviation
A | - | -
B | 0.206 | 0.027
C | - | -
D | 0.119 | 0.019
Parameter | Estimation | Standard deviation
A | - | -
B | 0.201 | 0.020
C | - | -
D | - | -
2nd iteration is performed which yielded the following results.
Parameter A and C are fixed from 1st iteration and only B and D further evaluated.
Parameter D yielded a value with standard deviation of less than 0.02
Parameter D is also fixed after 2nd iteration. 3rd iteration is done to find out B value.
3rd iteration yielded a value for parameter B with a standard deviation of 0.020
This concludes the total analysis.

## Slide 35: OVERBREAK MODEL
The constants values are A= 0.034, B =0.206, C =-0.017, D = 0.119
The equation becomes OB = 0.034* (L blast)0.206 -0.017*ln(RMR) + 0.119.
This developed model is to be tested using data from main tunnel 3.
Another factor influencing the quality of the parameter estimates is the number of data, therefore to verify the stability of the results with reference to the number of measurements used for the calculation forward regression is carried out.
This procedure allows the identification of the minimum number of data needed for a stable and accurate identification of the model parameters through the non-linear regression carried out.
Chart: Forward Regression Analysis
| 10 | 20 | 30 | 40 | 50 | 60 | 70
A | 0.012 | 0.018 | 0.021 | 0.031 | 0.032 | 0.034 | 0.034
B | -0.9 | -0.75 | -0.51 | -0.21 | -0.06 | 0.09 | 0.2
C | 0.15 | 0.02 | -0.04 | -0.012 | -0.013 | -0.015 | -0.017
D | -0.7 | -0.5 | -0.38 | -0.18 | 0.103 | 0.109 | 0.119

## Slide 36: Overbreak Model
From the above graph it is observed that the results become stable by using at least 60 measurements. However, an initial stabilization of results can already be observed starting from 30 measurements for parameters A and C
For parameter D, calculated value after 60 measurements did not change much unlike parameter B.
Moving forward, more data sets are required to be fed to further sharpen the estimate of B.
20 more datasets were further added to forward regression analysis and the following results were yielded.
Chart: Forward Regression Analysis
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90
A | 0.012 | 0.018 | 0.021 | 0.031 | 0.032 | 0.034 | 0.034 | 0.034 | 0.035
B | -0.9 | -0.75 | -0.51 | -0.21 | -0.06 | 0.09 | 0.2 | 0.21 | 0.22
C | 0.15 | 0.02 | -0.04 | -0.012 | -0.013 | -0.015 | -0.017 | -0.019 | -0.018
D | -0.7 | -0.5 | -0.38 | -0.18 | 0.103 | 0.109 | 0.119 | 0.139 | 0.136

## Slide 37: Overbreak Model
The values of parameter B and D stabilised further after 80 observations.
B value was finally fixed at 0.22 as value at 80 observations and 90 observations were almost similar.
The final values of all parameters are A = 0.035, B = 0.22, C = -0.018, D = 0.214.
The final equation of model is OB = 0.035* (L blast)0.22 -0.018*ln(RMR) + 0.214
Model Validation
The overbreak model obtained above was subsequently applied to the main tunnel 3 for validating the developed model.
Tunnel -3 was not used in developing the model and was kept aside for sole purpose of model validation.
To validate the model 9 blast results and their parameters were used. From the equation developed overbreak is derived. This obtained overbreak from the equation is them compared with actual overbreak which occurred at the blast and the variation is observed.
The results are shown in 3 separate formats for technical overbreak, geological overbreak and total overbreak.

## Slide 38: Overbreak Model Validation
Chart: Technical Overbreak Validation
Model | 3.24 | 7.21 | 4.92 | 5.21 | 3.92 | 4.15 | 6.24 | 5.81 | 4.92
Actual | 2.7 | 9.21 | 5.39 | 5.29 | 3.24 | 4.02 | 6.48 | 5.63 | 4.57
Chart: Geological Overbreak Validation
Model | 7.21 | 2.92 | 8.21 | 6.29 | 5.45 | 6.71 | 3.18 | 4.36 | 6.08
Actual | 5.96 | 2.88 | 8.95 | 6.03 | 5.89 | 6.98 | 3.87 | 2.95 | 6.91

## Slide 39: Overbreak Model Validation
The above figures show the model validation with data from the tunnel 3 for 2 types of overbreak.
Inspection of above figures shows that the developed model has very well approximated the total overbreak as well as its components (geological and technical).
The proposed model seems well equipped to estimate volumes of overbreak starting from drill-and-blast tunnelling. Unlike previous attempts to predict blast-induced overbreak, it is able to clearly differentiate technical from geological components, an important aspect in the definition of contracts.
Chart: Total Overbreak Validation
Model | 10.45 | 10.13 | 13.13 | 11.5 | 9.37 | 10.86 | 9.42 | 10.17 | 11
Actual | 8.66 | 12.09 | 14.34 | 11.32 | 9.13 | 11 | 10.35 | 8.58 | 11.48

## Slide 40: RESULTS
Charts relating overbreak damage to PPV are prepared for each rock class B2,B3,C1,C2 to read off overbreak.
Overbreak model distinguishing between technical and geological was proposed considering geological factors.
Developed model using Levenberg–Marquardt algorithm is OB = 0.035* (L blast)0.22 -0.018*ln(RMR) + 0.214
Technical overbreak is dependent on blast hole length while geological overbreak is dependent on RMR.
Amount of cycle time saved on application on soft blast techniques (proposed in last semester) was calculated.
Cycle time reduced for all rock classes but its magnitude was greater in rock class B2; highest being for main tunnel 3 of duration 2.35hours.
Activities which reduced cycle time are mucking, chipping and rock support installation.

## Slide 41: REFERNCES
Holmberg R, Persson PA. The Swedish approach to contour blasting. In: Proceedings of conference on explosives and blasting technique. New Orleans: Society of Explosives Engineers; 1978. p. 113–27.
6] Forsyth WW. A discussion of blast-induced overbreak in underground excavations. In: 4th International symposium, rock fragmentation by blasting. Vienna: Austria. p. 161–6.
Silva, J., Worsey, T., & Lusk, B. (2019). Practical assessment of rock damage due to blasting. International Journal of Mining Science and Technology, 29(3), 379-385.
Dey, K., & Murthy, V. M. S. R. (2012). Prediction of blast-induced overbreak from uncontrolled burn-cut blasting in tunnels driven through medium rock class. Tunnelling and Underground Space Technology, 28, 49-56.]
Murthy, V. M. S. R., Kaushik Dey, and Rajesh Raitani. "Prediction of overbreak in underground tunnel blasting: a case study."
Foderà, G. M., et al. "Factors influencing overbreak volumes in drill-and-blast tunnel excavation. A statistical analysis applied to the case study of the Brenner Base Tunnel–BBT." Tunnelling and Underground Space Technology 105 (2020): 103475.
Bogdanoff, Ingvar, 1996. Vibration measurements in the damage zone in tunnel blasting. In: Mohanty (Ed.), International Symposium on Rock Fragmentation by Blasting. Balkema, Rotterdam, pp. 177– 185.
Yang, R.L., Bawden, W.F., Talebi, S., Rocque, P., 1993a. An integrate technique for vibration monitoring adjacent to a blast hole. Can. Min. Metall. Bull. 86 (972).